## Slide 1: QUALITY CONTROL
OVERVIEW

## Slide 2: PURPOSE
  Understanding QC function
  Various tests that are performed
  Understanding the category of tests
  Significance of/reason for performing the tests

## Slide 3: What we do in Quality control
  QC will receive the samples for the testing from various departments with the sample testing requests. upon receiving the requests QC will enter those in the respected LOGs and proceed for the
  Testing of Packing materials
  Testing of Raw materials- API
  Testing of Raw materials- Excipients
  Testing of Microbiological samples
  Testing of In-process materials
  Testing of Finished goods
  Testing of Stability samples
  Classification of tests-1.Identification tests 2.Tests for strength/content
  3.purity(control of impurities) 4.Functionality tests.

## Slide 4: Identification tests
These tests are designed to verify the identity of the material. e.g. chemical structure, optical isomer, crystal form, salt etc.
At least two tests based on different analytical techniques are required to be part of specification.
Identification of each container is often performed to rule out mix-up (Rapid techniques like NIR or Raman spectroscopy are often used for such 100% ID.)

## Slide 5: Tests for strength /content
The test is commonly called as Assay and is designed to establish the strength or the purity of the material.
Primary methods like Titrimetry or secondary methods like HPLC,GC etc.are used to determine the Assay.
Limits are defined based on the variability expected in the material and analytical variability.
Assay is often expressed on anhydrous basis. In such cases determination of water content or Loss on drying is performed on the sample and the result is used to express the assay on anhydrous tests.

## Slide 6: Purity(Control of Impurities)
While Assay gives idea about gross purity of the material,it is important to ensure that the material is free from unwanted impurities which can come from the source or the process.
These tests are designed to detect and quantify the impurities which are likely to be present in the material.
The impurities can include-
1.chemical impurities coming from the starting materials or formed
during the manufacturing process.
2.Residual solvents, unwanted isomers, Metallic impurities which
may come from the catalysts or from the equipment.
3.Microbial contamination.

## Slide 7: Functionality/Efficacy tests
Apart from the chemical purity some materials have to have other specific characteristics to produce desired effect.
Functionality tests are designed to evaluate such characteristics.
  These tests are include but not limited to
    Particle size distribution
    Bulk density
    Polymorphism
    viscosity
    Solubility
    pH

## Slide 8: Chromatography(Meaning and principle)
Chromatography is derived from kromatos- colour and graphos-written.
Chromatography is classified into
1.Gas chromatography (GLC & GSC)
2.Liquid chromatography(LLC &LSC)
Separation of substances at molecular levels.
This is achieved using attraction or repulsion of the phases to be separated towards the stationary phase.
Mobile phase-gas or liquid
Stationary phase-liquid or solid.

## Slide 9: Tswetts Equipment Origin of chromatography
  Tall glass open filled with silica gel.
  Ground-up plant extracts
  Poured into the column and saw colored “Bands”
  Chroma- colour
  Graphy – writing/study of

## Slide 10: THANK YOU